MM SYSTEMS CORPORATION

GUIDELINE SPECIFICATIONS

DECORATIVE METAL COLUMN COVERS
DIVISION 5

PART 1 - GENERAL

1.1 RELATED DOCUMENTS

A. Drawings and General Provisions of the Contract, including General and Supplementary Conditions and Division 1 Specifications Sections apply to this Section.

1.2 SUMMARY

A. This section includes Metal Column Covers as shown on drawings.

B. Related Section include the following:

1.3 SUBMITTALS

A. Manufacturer's Literature and Data:

Product Data: Submit manufacturer's technical data and brochures for each type of column cover required.

B. Shop Drawings:

Shop drawings shall show dimensions, sizes, thickness, alloys, tempers, finishes, joining, attachments, and relationship of adjoining work.

C. Samples:

Samples shall include 3" x 5" piece of each type of metal and finish as specified.

D. Certification:

Submit certificates from manufacturer of column covers attesting that products comply with specified requirements including finish as specified.

F. Qualification Data:

The firms specified in the "Quality Assurance" Article, shall demonstrate their capabilities and experience by including lists of completed projects with project names and addresses, names and addresses of architects and owners, and other information specified.

1.4 QUALITY ASSURANCE

A. Manufacturer: Firm with manufacturing and delivery capacity required for the project, shall have successfully completed at least ten projects within the past five years, utilizing systems, materials and techniques as herein specified.

B. Fabricator must own and operate its own manufacturing facilities for all metal components. "Stick Build" or "Kit of Parts Systems" consisting of components from a variety of manufacturers will not be considered or accepted.

C. Manufacturer/Fabricator must own and operate its own Painting and Finishing facility to assure single source responsibility and quality control.

1.5 DELIVERY, STORAGE & HANDLING

All material shall be protected during fabrication, shipment, site storage and erection to prevent damage to the finished work from other trades. Store column covers inside a well ventilated area, away from uncured concrete and masonry, and protected from weather, moisture, soiling, abrasion, extreme temperatures, and humidity.

PART 2 - PRODUCTS

2.1 MANUFACTURER

A. Column covers shall be manufactured by MM Systems Corporation, 50 MM Way, Pendergrass, GA  30567 - 800-241-3460  or 706-824-7500.

B. The listed manufacturer shall not be construed as closing specifications to other prospective manufacturers, but rather as establishing a level of quality in a column cover system. Other systems may be submitted for approval as provided for in the specification at least 10 working days prior to submission of bids. Companies desiring to submit a proposal shall submit all descriptive information of the system proposed including photographs and shop drawings of at least three projects similar in detail and scope.

2.2 MATERIALS

Column Cover System shall be MM Systems Custom Column Cover System. All anchors clips and fasteners are to be provided as complete package of this work. No exposed fasteners for metal closures are allowed.

Aluminum sheet shall be 3003-H14 alloy, minimum .125". [ASTM B 209 (ASTM B 209M)]
Stainless steel sheet shall be Type 304, Minimum .064" (16 Gauge). [ASTM A 666]
Bronze sheet shall be Muntz metal alloy C280, Minimum .125". [ASTM B 36/B 36M]

2.3 FABRICATION

A. Height of column covers shall be up to 12'-0" without horizontal joints. Minimum radius is 6” in aluminum, and 7” in stainless steel (for smaller radii, contact MM Systems Corporation for solutions).

B. Column covers shall have either a vertical V-groove butt joint (VG Series), vertical reveal joint (VR Series), or field-spackled seamless joint (HJ Series) as shown on the architectural drawings. All other details including base and ceiling details shall be fabricated in accordance with the architectural drawings.

C. Column cover shall be manufactured true to geometry as shown on plan view of architectural drawings with a tolerance of +/- 1/16".

D. VG Series Column Covers

VG Series Column Covers shall be fabricated with return flanges at the vertical joints for structural strength with keyhole connection hidden fasteners.

E. VR Series Column Covers

VR Series Column Covers shall be fabricated with return flanges at the vertical joints for structural strength with angles for mechanical attachment to supports. Optional reveal strip for concealment of fasteners.

F. HJ Series Column Covers

HJ Series Column Covers shall be fabricated with tapered flanges at the vertical joints for attachment with drywall screws, and tape and spackle for a hidden joint.

G. Support framing is required for attachment of the column covers to the sub-structure (provided by installer).

2.4 FINISHES

A. Fluoropolymer coating finish:

- Two-coat, shop-applied, baked-on fluoropolymer coating system based on Atochem North America, Inc. Kynar 500 resin or Ausimont U.S.A., Inc. Hylar 5000 resin (polyvinylidene fluoride, PVDF), formulated by a liscensed manufacturer and applied by manufacturer’s approved applicator to meet AAMA Publication 605.2-90.

- Coating system shall provide minimum 1.0 mil dry film thickness consisting of minimum 0.20 mil primer and minimum 0.80 mil color coat.

- Color shall be as selected by Architect from manufacturer’s standard colors.

B. Stainless Steel finish:

- #4 Directional brush finish.

- #8 Mirror polish finish.

- Other finishes available (contact MM Systems Corporation).

C. Chromate Conversion pretreatment for field painting.

1.	Used for field painting and for HJ Series Column Covers.

D. Other finishes include decorated metals and embossed metals. (Contact MM Systems Corporation for availability).

PART 3 - EXECUTION

3.1 INSTALLATION

A. Install column covers in accordance with manufacturer's written installation instructions and shop drawings.

B. Column covers shall be erected plumb, level, square, true to line, securely anchored, and in proper alignment and relationship to work for other trades.

C. Column covers shall be inspected before installation to be free from dents, scratches and other defects.

3.2 CLEANING

A. Removal of protective covering shall occur immediately after installation to prevent adhesive transfer.

B. Clean all surfaces following installation.

C. Maintain per manufacturer's finish maintenance instructions.

3.3 PROTECTION

A. Protection of column covers from damage by other trades after installation to be provided by general contractor.

Note To Specifier: Column Covers are a finished-decorative product, and should be installed by mechanics who are experienced in handling finished products. They may be specified in, Division 5 – Metals or Division 9 - Finishes.