# MM SYSTEMS CORPORATION

# TRENCH GRATES SPECIFICATIONS

# PART 1 — GENERAL

- RELATED DOCUMENTS

  - Drawings and general provisions of the Contract, including General Conditions, Supplementary Conditions and Division-1 General Requirements, apply to the work of this section.

- WORK INCLUDED

  - Furnish and install complete MM Systems Corporation trench grate systems.

    - Aluminum trench grating and frames.

    - Bronze trench grating and frames.

    - Swimming Pool Deck Drains.

    - Trench Liners.

- RELATED WORK

  - Related work that is specified elsewhere.

    - Concrete work: Section 03000.

    - Cast-in-place Concrete: Section 03300.

    - Grout: Section 03600.

- REFERENCES

  - Publications listed herein are part of this specification to the extent referenced. The criteria established in the specifications shall take precedence over the standards referenced herein. (Examples of reference standards are given below.)

    - American Society for Testing and Materials (ASTM):

      - ASTM B 209, Standard Specification for Aluminum and Aluminum-Alloy Sheet and Plate

      - ASTM B 221, Standard Specification for Aluminum and Aluminum-Alloy Extruded Bars, Rods, Wire, Shapes and Tubes

      - ASTM A 666, Standard Specification for Austenitic Stainless Steel Sheet, Strip, Plate, and Flat Bar

      - ASTM B 455, Standard Specification for Copper-Zinc-Lead Alloy (Leaded-Brass) Extruded Shapes

- DEFINITIONS

  - Define industry and product terms as necessary.

- SYSTEM DESCRIPTION

  - [Trench grating] [Swimming pool deck grating] shall permit unrestrained drainage.

  - [Trench grating] [Swimming pool deck grating] shall permit pedestrian traffic over the grating.

  - Allowable loads on grating shall be 300 psf, the minimum required by the Uniform Load Test and the Point Load Test.

  - Grating shall be [traditional, with grating bars spanning across the trench] [linear, with grating bars running the length of the trench] [Unframed].

  - Trench grating may be locked down [Optional] so as to be flush with the finish flooring; locks shall be concealed and grating sections shall be independently removable.

- QUALITY ASSURANCE

  - Manufacturer: Furnish assemblies from one (1) manufacturer.

  - Installer: Firm with not less than three (3) years of successful experience in the installation of systems similar to those required by this project and acceptable to the manufacturer of the system.

- SUBMITTALS

  - Submissions must be made within ten (10) working days of the General Contract award to avoid project delay. If not adhered to, the Architect will designate the exact product to be used and the contractor will have no recourse.

    - Submit manufacturer’s specifications and technical data, including Material Safety Data Sheets, installation instructions, and, as required, catalog cuts and templates to explain construction and to provide for incorporation of the product into the project.

    - Submit shop drawings showing layout and types of [trench] [swimming pool deck] grates and frames; full-scale sections of typical installations; anchors and accessories. Shop drawings submittal shall be coordinated with concrete work.

    - Submit one (1) [6"] [12" x 12"] sample of the specified system.

- DELIVERY, STORAGE AND HANDLING

  - Deliver [trench grating] [swimming pool deck grating] [trench liner] to jobsite in new, clean, unopened crates of sufficient size and strength to protect materials during transit.

  - Store components in original containers in a clean, dry location.

  - Handle components with equipment of sufficient size to preclude hazard to personnel or damage to components.

- SEQUENCING

  - Submittals shall be completed and approved prior to award of subcontract for system components.

  - Subcontract for the work of this section shall be planned to allow sufficient time for manufacturer’s production and delivery scheduling.

- WARRANTY

  - Submit manufacturer’s warranty that materials furnished will perform as specified for a period of not less than one (1) year when installed in accordance with the manufacturer’s recommendations.

# PART 2 — PRODUCTS

- ACCEPTABLE MANUFACTURERS

  - Furnish and install as noted in specifications and as indicated on drawings, [Trench grating system (type no.)] [Swimming pool deck grating system (type no.)] [Trench liner system (type no.)] as manufactured by: MM Systems Corporation, 50 MM Way, Pendergrass, GA. 30567; phone: 800-241-3460 or (706) 824-7500; fax: (706) 824-7501.

  - The products herein specified are [standard] [custom] manufactured products of the listed manufacturer. The system has been carefully selected to produce functional and aesthetic considerations specified herein.

  - Substitutions: Submit proposed substitutions in writing to the Architect no less than 10 days before bids are due. Submit samples and product data to demonstrate the acceptability of proposed substitute. Acceptance will be by Addendum.

- MATERIALS

  - [Trench grating] [Swimming pool deck grating] and frames: [Manufacturer and type number] [proprietary product name].

    - Aluminum: ASTM B 221, alloy 6061-T6 for extrusions.

    - Bronze alloy C38500, for extrusions and angle.

  - Trench liners: [Manufacturer and type number]

    - Galvanized Steel G90, [20 gauge] [_____ gauge].

    - Aluminum: ASTM B 209, alloy 5052-H32, [16 gauge] [_____ gauge].

    - Stainless Steel, ASTM A 666, type 304, [22 gauge] [_____ gauge].

  - Fasteners, accessories and other materials required for complete installation in accordance with the manufacturer’s installation instructions.

  - Abrasive, rough texture, non-slip coating available in custom colors. Color shall be: ____________________.

- FABRICATION

  - Fabricate [trench grating] [swimming pool deck grating] [trench liner] assemblies as detailed.

    - Fabricate [trench grating] [swimming pool deck grating] [trench liner] [__________] inches wide.

    - Fabricate trench grating tread bars spaced 1/2" o.c. with the maximum space between bars to be 1/4 inch.

    - Fabricate custom radius grating sections as required.

    - Tread surfaces shall be [serrated] [plain] [abrasive coated].

    - Provide concealed locking mechanisms.

    - Provide necessary and related parts, devices, trench liner, anchors and other items required for water-resistant installations.

    - Fabricate splices, corner units, corner fittings, intersections and end closures as required.

    - Miter and weld joints shall be factory manufactured.

  - Provide components in single size where possible; minimize site splicing.

    - Fabricate grating units to maximum size recommended by the manufacturer for units intended for removal and cleaning. If joints are necessary in the grating, they shall be spaced symmetrically and away from normal traffic flow patterns.

    - Provide minimum number of pieces possible for frames that exceed maximum length. Provide frames with hairline joints, equally spaced, complete with corner pin, splice plates and installation anchors.

    - Frame shall be shop fabricated as an assembled unit for installation in the field.

  - Shop assemble components and package with anchors and fittings.

- FINISHES

  - Aluminum:

    - Exposed aluminum surfaces shall be [mill finish] [204-R1 clear anodized finish].

  - Bronze:

    - Unexposed bronze surfaces shall be mill finish.

  - Abrasive shall be [black] [custom color]..

# PART 3 — EXECUTION

- EXAMINATION

  - Contractor shall verify that field measurements [and recessed dimensions] are as shown on shop drawings prior to releasing materials for fabrication by the manufacturer.

  - Installer shall examine conditions under which work is to be performed and shall notify the contractor in writing of unsatisfactory conditions. Installer shall not proceed until unsatisfactory conditions have been corrected in a manner acceptable to the installer.

- INSTALLATION

  - Install [Trench grating system] [Trench liner system] [Swimming pool grate system] in accordance with the governing regulations, the industry standards applicable to the work and the manufacturer’s written installation instructions.

  - [Trench grating] [Swimming pool deck grating] shall be [blockout] [cast-in-place].

  - Trench liners shall be [rigidly anchored to trench frame] [cast-in-place].

  - Work shall be aligned plumb, level, and, where required, flush with adjacent surfaces.

- CLEANING

  - Clean exposed surfaces as recommended by the manufacturer.

- ADJUSTING AND PROTECTION

  - Inspect system components for proper fit. Adjust, repair or replace components not conforming to requirements. Repair or replacement of an individual unit shall be as approved by the Architect.

  - Advise the contractor of procedures required to protect the finished work from damage during the remainder of the construction period.

  - Finished units shall be without damage. The contractor at their expense shall repair units damaged during construction.

  - Protect installation from damage by work of other Sections. After installation of the frame, install temporary filler of plywood in recesses, and cover the frames with plywood protective flooring. Maintain protection until construction traffic has ended and the project is near time of Substantial Completion.

  - Install grating near time of Substantial Completion.

- GENERAL RESPONSIBILITY

  - Any variation from this specification resulting in additional cost to any other contractor or subcontractor on this project shall be the sole financial responsibility of the contractor for the work of this section.

- SCHEDULE

  - Indicate MM Systems Corporation product number on Drawings or Schedule.

    - Interior Trench Grating: __________

    - Exterior Trench Grating: __________

    - Interior Swimming Pool Boundary Grating: __________

    - Exterior Swimming Pool Boundary Grating: __________

    - Interior Trench Liner: __________

    - Exterior Trench Liner: __________